## Slide 1
ARDUINO
RAIN DETECTION SYSTEM
A step-by-step build presentation
Rain sensor • LED alert • Buzzer • 10-second auto-off
PROJECT PRESENTATION
Prepared for an academic electronics project
01

## Slide 2
RAIN DETECTION SYSTEM
01
ARDUINO RAIN DETECTION SYSTEM

## Slide 3
Project overview
01 • INTRODUCTION
02
A small embedded system that senses water and gives a short visual + audible alert.
01 SENSE
Rain sensor detects moisture on its sensing plate.
Arduino reads the analogue value at A0.
02 ALERT
If the reading crosses the chosen threshold:
• LED turns ON
• Buzzer sounds
03 AUTO-OFF
Alarm turns OFF after 10 seconds.
System waits for the sensor to become dry before it can trigger again.
PROJECT GOAL
Build a low-cost, beginner-friendly rain alert and learn sensor input, output control, timing, and circuit wiring.
ARDUINO RAIN DETECTION SYSTEM

## Slide 4
Components required
02 • PREPARE
03
Arduino Uno
Main controller; reads the sensor and controls outputs.
Rain sensor module
Sensing plate + module; use AO for analogue readings.
Active buzzer
Provides audible alert. Code below assumes an active buzzer.
Small LED + 220Ω
Visual alert; resistor limits current through the LED.
Breadboard + jumpers
Temporary connections without soldering.
USB cable / power
Upload code and power the Arduino during testing.
Optional: a high-power white torch LED is different from a small indicator LED and needs a suitable driver and power supply.
ARDUINO RAIN DETECTION SYSTEM

## Slide 5
How the system is connected
03 • SYSTEM DESIGN
04
RAIN SENSOR
Water / moisture Analogue signal
ARDUINO UNO
Reads A0 Runs decision + timer
LED
Visual alert D8 through resistor
BUZZER
Sound alert D3
Power and GND are shared appropriately; all modules must share a common GND.
SIGNAL FLOW
Sensor reading → threshold check → outputs ON → 10-second timer → outputs OFF
ARDUINO RAIN DETECTION SYSTEM

## Slide 6
Wiring: make each connection
04 • BUILD
05
COMPONENT / PIN | CONNECT TO | PURPOSE
Rain sensor VCC | Arduino 5V | Power for sensor module
Rain sensor GND | Arduino GND | Common ground
Rain sensor AO | Arduino A0 | Analogue sensor reading
Buzzer + | Arduino D3 | Active buzzer control
Buzzer − | Arduino GND | Return path
Arduino D8 | 220Ω resistor → LED long leg (+) | LED current limited by resistor
LED short leg (−) | Arduino GND | Ground connection
LED rule: long leg = positive; short leg = GND. Do not omit the resistor.
ARDUINO RAIN DETECTION SYSTEM

## Slide 7
Breadboard and safe wiring tips
04 • BUILD
06
Use the ground rail
Connect one Arduino GND pin to the breadboard’s negative (−) rail.
Connect the sensor, buzzer, LED and other GND wires to that rail.
Check that separate rails are linked if needed.
Protect the hardware
Power off before changing wiring.
Use a 220Ω resistor in series with the small LED.
Never connect a battery directly to the 5V pin unless it is a regulated 5V supply.
About a white torch LED
A high-power torch LED must not be driven directly from D8. It may need a suitable transistor/MOSFET driver, current limiting, and an appropriate external supply.
About the buzzer
This example assumes an active buzzer that sounds when driven HIGH. A passive buzzer may need tone() / noTone(). Avoid drawing excessive current from an Arduino pin.
ARDUINO RAIN DETECTION SYSTEM

## Slide 8
Program logic: from water to alarm
05 • LOGIC
07
START / SETUP
Set D3, D8 as outputs
READ SENSOR
Read analogue A0
CHECK THRESHOLD
Is value < 1000?
START ALARM
If not already started
10 SECONDS ELAPSED?
Turn LED + buzzer OFF
SENSOR DRY?
Reset for next detection
REPEAT LOOP
Read again after 100 ms
Important behavior: after the alarm times out, it stays OFF while the sensor remains wet. It rearms only after the reading returns to the dry range.
ARDUINO RAIN DETECTION SYSTEM

## Slide 9
Arduino code (1/2): setup and trigger
06 • CODE
08
#define BUZZER_PIN 3 #define LED_PIN 8 bool alarmStarted = false; unsigned long alarmStartTime = 0; void setup() { pinMode(BUZZER_PIN, OUTPUT); pinMode(LED_PIN, OUTPUT); Serial.begin(9600); } void loop() { int sensorValue = analogRead(A0); Serial.println(sensorValue); // Start only once when wet is first detected if (sensorValue < 1000 && alarmStarted == false) { alarmStarted = true; alarmStartTime = millis(); digitalWrite(LED_PIN, HIGH); digitalWrite(BUZZER_PIN, HIGH); }
ARDUINO RAIN DETECTION SYSTEM

## Slide 10
Arduino code (2/2): timeout and reset
06 • CODE
09
// Turn outputs OFF after 10 seconds if (alarmStarted == true && millis() - alarmStartTime >= 10000) { digitalWrite(LED_PIN, LOW); digitalWrite(BUZZER_PIN, LOW); } // Reset only after the sensor becomes dry if (sensorValue >= 1000) { alarmStarted = false; digitalWrite(LED_PIN, LOW); digitalWrite(BUZZER_PIN, LOW); } delay(100); }
10,000 milliseconds = 10 seconds
millis() measures elapsed time without blocking the sensor loop.
Why use a state flag?
alarmStarted prevents the timer from restarting continuously while the sensor stays wet.
ARDUINO RAIN DETECTION SYSTEM

## Slide 11
Calibrate and test the sensor
07 • TEST
10
1 DRY TEST
Upload the code. Open Serial Monitor and set baud rate to 9600. Record the dry readings.
2 WET TEST
Add a few drops of water to the sensing plate. Record the wet readings.
3 SET THRESHOLD
Choose a value between the observed dry and wet readings. Example: 500 only if readings support it.
Illustrative readings only — your sensor may differ
Condition | Example reading | If threshold is 500
Dry | 900 | No alarm
Wet | 300 | Alarm starts
If dry readings are also below 500, the alarm may trigger unexpectedly; adjust the threshold after testing.
ARDUINO RAIN DETECTION SYSTEM

## Slide 12
Expected result and verification
07 • TEST
11
DRY
LED OFF • Buzzer OFF
WATER DETECTED
LED ON • Buzzer ON
AFTER 10 SECONDS
LED OFF • Buzzer OFF
STILL WET
Alarm remains OFF
SENSOR DRIES
System rearms for next event
ARDUINO RAIN DETECTION SYSTEM

## Slide 13
Troubleshooting checklist
08 • DEBUG
12
LED never lights
Check LED polarity, resistor, D8, and GND.
Buzzer stays silent
Confirm active buzzer type, polarity, D3 and GND; test buzzer separately.
Alarm triggers while dry
Read Serial Monitor and raise/lower threshold based on measured values.
Alarm never triggers
Check sensor AO → A0, sensor VCC/GND, and wet readings.
Switch not used
This version intentionally has no switch; it auto-silences after 10 seconds.
ARDUINO RAIN DETECTION SYSTEM

## Slide 14
PROJECT SUMMARY
Sense. Decide. Alert. Reset.
The Arduino reads the rain sensor, activates a light and buzzer when the measured value crosses a calibrated threshold, and automatically silences the alarm after 10 seconds.
INPUT
Rain sensor on A0
PROCESS
Threshold + timer
OUTPUT
LED on D8 + buzzer D3
14
ARDUINO RAIN DETECTION SYSTEM

## Slide 15
PROCESS
OUTPUT
Thank you
14
ARDUINO RAIN DETECTION SYSTEM